## Slide 1
Introduction
to
TCP/IP protocol Suite
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in

## Slide 2: Protocol Layering
In data communication and networking, a Protocol defines the rules that both the sender and receiver and all intermediate devices need to follow to be able to communicate effectively.
When communication is simple, we may need only one simple protocol.
When communication is complex, we may need to divide the task between different layers, in which case we need a protocol at each layer, or Protocol Layering.
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 3: A Single Layer protocol
Greet eachother when they meet
Confine the vocabulary to the level of friendship
Refrain from speaking if one is speaking
Opportunity to talk both on an issue (dialog / monolog)
Exchange nice words when departing
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 4: A three-Layer Protocol
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 5: Principles of Protocol layering
First principle: If we want bidirectional communications, we need to make each layer so that it is able to perform two opposite tasks, one in each direction.
Second Principle: Two objects under each layer at both side should be identical.
Logical connection between peer layers
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 6: Introduction
TCP/IP is a protocol suite used in the Internet today. It’s a hierarchical protocol made up of interactive modules, each of which provides a specific functionality.
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Image Source: Weblink https://www.google.com/url?sa=i&source=images&cd=&ved=2ahUKEwjspoq34s7fAhVJbn0KHaFSBdMQjRx6BAgBEAU&url=https%3A%2F%2Fwww.youtube.com%2Fwatch%3Fv%3DS9NhTS0WssI&psig=AOvVaw2rl2F6guAkQrGI6I02i1PW&ust=1546507202644930

## Slide 7: Communication through an internet
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 8: Layers in the TCP/Ip protocol suite
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 9: Identical objects in the TCp/ip protocol suite
Source: Data Communications and Networking 5E, Forouzan
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in

## Slide 10: Physical Layer
1. Physical Characteristics of Interface and medium : Type of Transmission medium
2. Representation of Bits : Encoding Techniques ; Conversion of Bits to Electrical/Optical signals
3. Data rate: bits/sec
4. Synchronization: Clock Synchronization at Sender & receiver
5. Physical Topology: Star, Bus, Mesh, Ring etc
6. Line Configuration : Point to Point, Multipoint Configurations
7. Transmission Mode : Simplex , Half-Duplex, Full-Duplex
Physical layer is responsible for movements of bits from one hop(node) to the next
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan
Image Source: https://slideplayer.com/slide/9415506/

## Slide 11: Data Link Layer
1. Framing
2. Physical Addressing
3.Flow control
4. Error Control: Detection & Correction
5. Access Control
Data link layer is responsible for moving frames from one hop(node) to the next
e.g., ARP, IEEE 802.3 and IEEE 802.11
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan
Image Source: http://www.highteck.net/EN/DataLink/Data_Link_Layer.html

## Slide 12: Network Layer
1. Logical Addressing: IPv4, IPv6
2. Routing: Routing algorithms & table (traffic routing & control)
Network layer is responsible for delivery of individual packets from source host to destination host
e.g., IP, ICMP, IGMP, DHCP
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan
Image Source: Weblink
https://fossbytes.com/network-layer-osi-model/

## Slide 13: Transport Layer
1. Service point addressing: Port Address
2. Segmentation : Divided into transmittable segments with sequence numbers
3. Connection Control
4. Flow Control
5. Session Multiplexing
6. Error Detection & Correction (resends)
7. Message reordering (reassembly)
Transport layer is responsible for the delivery of the message from one process to another
e.g., TCP, UDP
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 14: Application Layer
1. Network virtual terminal (e.g. usgs)
2.File transfer, access and management
3.Mail services
4.Directory services
Application layer is responsible for providing services to the user.
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan
Image Socure: https://www.pinterest.com/pin/561050066049773076/?lp=true

## Slide 15
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Source: Data Communications and Networking 5E, Forouzan

## Slide 16
Relationship of layers and
Addresses in TCP/IP
Specific Address
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in
Image Source : https://slideplayer.com/slide/5357044/

## Slide 17
Thank you very much
Hope Foundation’s International Institute of Information Technology, I²IT, P-14 Rajiv Gandhi Infotech Park, Hinjawadi, Pune - 411 057
Tel - +91 20 22933441 / 2 / 3 | Website - www.isquareit.edu.in ; Email - info@isquareit.edu.in