## Slide 1: power budget analysis for Fiber optics link part 2
Prof. Bhagyashri Thorat
Assistant Professor
Department of Electronics & Telecommunication
Hope Foundation’s International Institute of Information Technology

## Slide 2: Optical power loss model
A typical optical power loss model for a point- to- point link considered
one transmitter,
one receiver
two connectors & splices as shown in figure

## Slide 4
The total optical power received at photodetector is equal to losses occuring in fiber, connetor , splices & loss of light coupled into fiber from transmitter.
The loss budget is nothing but summation of above losses mention. Each of these loss elements is expressed in decibels (dB) as,
Where,

## Slide 5
The total link loss budget is equal to differenence between optical power emering from the end of a fiber flylead attached to the light source and receiver sensitivity .

## Slide 6: Link power margin or system margin
Link Power analysis is capable to provide analysis which gives compnent aging, temperature fluctuations and losses arising from components that are going to add in future.
This addition in link budget is called link power margin, normally its between range 3 to 6 dB.

## Slide 7
Thank You
For further details please feel free to contact
Bhagyashri Thorat
Department of Electronics & Telecommunication
Hope Foundation’s
International Institute of Information Technology, I²IT
P-14, Rajiv Gandhi Infotech Park, MIDC Phase 1,
Hinjawadi, Pune – 411 057
Tel +91 20 22933441 / 2 /3
www.isquareit.edu.in
bhagyashrit@isquareit.edu.in | info@isquareit.edu.in