## Slide 1
Prof. Ashvini Kulkarni
Electronics & Telecommunication
International Institute of Information Technology, I²IT
www.isquareit.edu.in
Interrupt Handling with LPC2148

## Slide 2
  Introduction to Interrupts in ARM processors
  IRQ
  FIQ
  Associated Registers with interrupts
  Interrupt Enabling
  Sample ISR
  References
Syllabus

## Slide 3
Any event that disturb flow of execution (Event can be internal /external)
Interrupts
Vectored
Non-vectored
FIQ
IRQ
Interrupts are Handled by Vectored Interrupt Controller(VIC) in LPC2148
Interrupts

## Slide 4
Types of Interrupts in LPC2148
Fast Interrupt Request i.e FIQ : which has highest priority
Vectored Interrupt Request i.e Vectored IRQ : which has ‘middle’ or priority between FIQ and Non-Vectored IRQ.
Non-Vectored IRQ : which has the lowest priority.

## Slide 5
Vectored, Non-Vectored Interrupts
What does mean ?
‘Vectored‘ means that the CPU of LPC2148 is aware of the address of the ISR(Interrupt Service Routine) when the interrupt occurs
**For the Vectored interrupts , the System internally maintains a table called IVT (Interrupt Vector Table )which contains the information about Interrupts sources and their corresponding ISR address.
‘Non-Vectored‘ means that CPU of LPC2148 doesn’t know the address of the ISR(Interrupt Service Routine) nor the source of the IRQ when the interrupt occurs.
**CPU needs to be supplied by the ISR address.

## Slide 6
Interrupt Sources in lpc2148
There are 32 Interrupt Sources in LPC2148
32 interrupts are program and categorised into 3 ways
    FIQ
    Vectored IRQ
    Non-vectored IRQ
But there are only 16 Slots in in the Vectored
Vectored Interrupt Controller (VIC) 0 to 15 has 16 slots.
    Slot 0 Highest Priority
    Slot 15 Lowest Priority

## Slide 7
Registers Involved
VICIntSelect (R/W)0 = IRQ, 1 = FIQ
VICIntEnable (R/W) Enable Selective Interrupt Source
VICIntEnClr (R/W) Disable Selective Interrupt Source
VICIRQStatus (R) to know the status of enabled interrupt
VICFIQStatus (R) to know the status of enabled FIQ
VICSoftInt to trigger a software interrupt
VICSoftIntClear to clear software interrupt
VICVectCntl0 to VICVectCntl15 Assign interrupt source
VICVectAddr0 to VICVectAddr15 Assign interrupt address
VICVectAddr Holds the address of currently active interrupt
VICDefVectAddr Holds the addressof Non-Vectored ISR

## Slide 8
How to Write an ISR?
Method – 1 Method – 2
__irq void myISR (void) void myISR (void) __irq
{ {
... ...
} }

## Slide 9
A Simple 3 Step Process to Enable a Vectored IRQ
Step – 1 : Enable the IRQ by setting the appropriate bit of VICIntEnable to ’1′.
Step-2 : Identify the interrupt source number and assign it to VICVectCntlX.
Step-3 : Assign the address of the related ISR to VICVectAddrX.

## Slide 10
Interrupt Enabling
First VICIntEnable, from Table we get the bit number to Enable Interrupt with its Bit number. Ex. ADC0 interrupt--Hence we must make bit 18 in VICIntEnable to ’1′.
Second , from Table we get the interrupt source number for ADC0 which is decimal 18 and OR it with (1<<5) [i.e 5th bit=1 which enables the slot] and assign it to VICVectCntlX.
Third, Next assign the address of the related ISR to VICVectAddrX.

## Slide 11
Sample Interrupt Initialization
VICIntEnable= (1<<18);
VICVectCntl0=(1<<5)|18;
VICVectAddr0=(unsigned) adc0ISR;

## Slide 12
Sample ISR
  __ irq void adc0ISR(void)
  {
  Unsigned long ad0gdr_read=AD0DR3;
  Int digital = (ad0gdr_read>>6)&0x3ff;
  Dummyread=digital;
  VICVectAddr=0x0;
  }

## Slide 13
Important Note
If the vectored IRQ slot is disabled it will not disable the interrupt but will change the corresponding interrupt to Non-Vectored IRQ.
Enabling the slot here means that it can generate the address of the ‘dedicated Interrupt handling function (ISR)’
Disabling it will generate the address of the ‘common/default Interrupt handling function (ISR)’ which is for Non-Vectored ISR.
In simple words if the slot is enabled it points to ‘specific and dedicated interrupt handling function’ and if its disable it will point to the ‘default function’.

## Slide 14
References
[1] Andrew Sloss, Dominic Symes, Chris Wright, ―ARM System Developer‘s Guide – Designing and Optimizing System Software‖, ELSEVIER
[2]Trevor Martin- Insider’s guide to the philips ARM7-based Microcontrollers,Hitex
[3] www.arm .com
[4] Data sheet: LPC2148 User Manual

## Slide 15
THANK YOU
For further information please contact
Prof. Ashvini Kulkarni
Department of Electronics & Telecommunication
Hope Foundation’s International Institute of Information Technology, I²IT Hinjawadi, Pune – 411 057
Phone - +91 20 22933441
www.isquareit.edu.in | ashvinik@isquareit.edu.in | info@isquareit.edu.in