## Slide 1
Wireless Sensor Networks
Prof. Ravindra Joshi
Department of Engineering Sciences
International Institute of Information Technology, I²IT
www.isquareit.edu.in

## Slide 2
Agenda
Introduction to Wireless Sensor Networks (WSN)
Wireless Sensor Networks and Mobile Ad-hoc
Networks (MANETs)
Current Research in Wireless Sensor Networks
Key Challenges

## Slide 3
Wireless sensor networks
Wireless sensor network is a distributed system
consisting of a large number of low-cost wireless
sensor nodes equipped with a small processor with
limited memory, RF trans-receiver, antenna, sensing
elements and are powered with small batteries and
solar cells.
It’s a heterogeneous system, consisting of various types
of sensor nodes, actuators and operating systems.
Sensor nodes operate under constraints of memory,
size, computational power, overall cost and limited
energy sources such as batteries / solar cells.

## Slide 4
Wireless sensor networks
Main components are,
  Sensor nodes
  Sink nodes or base nodes
  Access points connecting WSN to the wired network
Sensor nodes
Sink nodes
Sink nodes
Sensor fields

## Slide 5
Components of Wireless sensor networks
Sensor node is a basic component in any wireless
sensor network.
  It consists of sensing, computing and communication
capabilities and also has an “on-board” power source.
  After the field deployment, sensor nodes communicate with
  each other with a multi-hop approach and collect information
  using either continuous or event driven modes.
  Location and positioning information is also exchanged with GPS
  or Local positioning algorithms.
  Global view of the phenomena or object is constructed after
processing the information collected from sensor nodes
  Once the battery get exhausted, sensor node can’t be used any
  further.

## Slide 6
Sink node (or base node) is another important
component in any wireless sensor network.
  They have enhanced capabilities such as more computational
  power, memory, energy, storage and communication capabilities
  All sensor nodes within a sensor field communicate with this
  base node periodically and to exchange the field information
  The processing capability of the individual node is limited but
  the aggregate processing power of the entire network is sizable.
  Sink nodes are connected to wired network through access points
  and act as interface between users and the sensor network.
  Users can inject queries and gather information of their interest
  from the base nodes.
Components of Wireless sensor networks

## Slide 7
Communication between sensor nodes
(b) Self-configuration transition
(a) Communication Hole
(c) Final State
Help Messages
Data Message
Sink
Source
Sink
Source
Neighbor Announcements
Messages
Data Message
Sink
Source
Active Neighbor
Passive Neighbor
The nodes can be in active or passive state:
  Active nodes forward data packets (using a routing mechanism
  that runs on the topology).
  Passive nodes do not forward packets but might sleep or collect network measurements.
  10 to 1000 nodes, 5 m to 50 m spacing between the nodes

## Slide 8
Applications of wireless sensor networks
Wireless Sensor Networks find numerous applications
in various areas as mentioned below,
Environment monitoring and protection:
  Monitoring of seismic activities/ data collection
  Warning of earthquakes and floods
  Weather monitoring and forecasting
Agricultural applications:
  Monitoring of soil humidity and temperature
  Detection of toxic levels in soil and water contamination
  Leakage in pipelines, risk of explosions for gas/oil pipelines
  Water pressure monitoring in dams and reservoirs
  Understanding of soil structure

## Slide 9
Protection of buildings:
  Fire alarms
  Burglar alarms/ Intruder detection
  Structural condition assessment of buildings, bridges
Military applications:
  Soldier tracking
  Battlefield tanks / vehicles tracking
  Invading remote and inaccessible areas
Industrial applications:
  Inventory control
  Process automation
Applications of wireless sensor networks

## Slide 10
Automotive Engineering:
  Monitoring of engine parameters
  Noise and pollution measurements
  Structural condition assessment of vehicles
Medical applications:
  Biomedical applications/ measurements
  Monitoring of human body with embedded sensors
Space applications:
  Automatic positioning
  Sensing of humidity, gravitational force
Marine Engineering:
  Study of marine life and water contamination
Applications of wireless sensor networks

## Slide 11
Information Processing in Wireless sensor networks
Processor Platforms
Radios
Sensors
Operating Systems
Localization
Time Synchronization
Medium Access
Calibration
Collaborative Signal Processing
Data-centric Routing
Data-centric Storage
Querying, Triggering
Aggregation and Compression
Collaborative Event Processing
Monitoring
Security

## Slide 12
Hardware: Platforms, Radios & sensors
Processors
  Atmel
  StrongARM
  X-Scale
Radios
  Chipcon CC1000
  Bluetooth
  Zigbee
Sensors
Platforms
  Mica-2
  Stargate
  iMote

## Slide 13
Processor comparison
 | Atmel ATMEGA128(L) | Strong ARM SA1100 | Intel XScale
Type | Micro Controller | Microprocessor | Microprocessor
Architecture | Harvard, 8-bit RISC | Harvard 32-bit RISC | Harvard 32-bit RISC
Speed | 8MHz/16MHz | 206MHz | 200/300/400 MHz
Cache/ Memory | 128KB programming memory 4KB data memory | 16KB instruction cache 8KB data cache | 32KB instruction cache 32KB data cache
Power Draw | run mode: 16.5mW sleep mode: < 60µW | run mode: 800 mW idle mode: 210 mW sleep mode: 50µW | run mode: 400 mW idle mode: 160mW sleep mode: 50µW
Example Platforms | Mica2 mote | Compaq iPAQ3700 | Compaq iPAQ3900

## Slide 14
Radios
Low power, short range
Relevant criteria
  Frequency
  Modulation scheme
  Encoding scheme
  Data rates
  Frequency diversity
Power considerations
  Receive power
  Transmit power
  For short range communication, the two are comparable

## Slide 15
Sensors
Small (coin, matchbox size) nodes with
  Processor
    8-bit processors to x86 class processors
  Memory
    Kbytes – Mbytes range
  Radio
    20-100 Kbps
Battery powered
Built-in sensors

## Slide 16
Operating systems
Depending the platform, various choices are available
  Tiny OS
  Embedded Linux
  -OS
Tiny OS is most suitable
  Developed by University of California, Berkley
  Event driven execution, No polling, No blocking
  Concurrency intensive operation, multi-threads based
  Light weight
  Easy to integrate with hardware

## Slide 17
Hardware platforms using Tiny OS
 | Crossbow mica | Crossbow mica 2 | Intel Mote
CPU | ATmega128L | ATmega128L(4MHz) | ARM core(12MHz)
Program memory | 128k Flash memory | 128k Flash memory | 512k Flash memory
Data Memory | 4K SRAM | 4K SRAM | 64K SRAM
Radio | RFM TR1000 | ChipCon CC1000 | Bluetooth
Data rate | 40 Kbps | 76.8 K Baud | 1 Mbps
Frequency | 916.50 MHz | 315/433/868/915MHz | 2.4 GHz

## Slide 18
Wireless sensor networks & MANETS
A mobile ad-hoc network (MANET) is a self-configuring
network of mobile routers and associated hosts connected
by wireless links.
The mobile routers are free to move randomly and organize
themselves arbitrarily, hence the network topology may
change rapidly and unpredictably.
This network may operate in stand alone manner or can
be connected to the Internet.
It has less number of nodes compared to the wireless
sensor network. E.g. communication between vehicles
and roadside equipment (VANETS)

## Slide 19
Comparison of WSN & MANET
WSN
More nodes are deployed (from
10 to 1000)
- Nodes have less processing power
Nodes are miniature, low cost and
can not be easily replaced once
battery runs out, as they are
distributed over larger distances
Nodes do not require human
interaction and can remain
unattended for a longer time
- Redundant information is collected
from neighboring nodes by the sink
MANET
Less number of nodes are
deployed (from 10 to 100)
Nodes have more processing
power and have less constraints
of memory, energy resources
etc.
Nodes can be expensive
and can be replaced, if required
Nodes are spread over less distances
Redundant information is not
collected by neighboring nodes

## Slide 20
Current research in wireless sensor networks
Optimization of network lifetime:
  Requires less transmission power to be used
  Trade-off between network lifetime and reliability
Minimize the battery consumption:
  Reduce the communication related and processing power
  Use of sleep/ inactive modes
Routing algorithms:
  Transmission power is closely related to the route selection
Algorithms for access control:
  They should consume minimum power

## Slide 21
Key technical challenges faced
Scalability of network protocols:
  Since the number of nodes are large
Designing simple, fast, efficient routing algorithms:
  Objective is to reduce the communication related power
  Optimum route selection between the available routes
  Fast convergence
  Less overheads
Distributed signal processing:
Mobility and security issues of the sensor nodes:

## Slide 22
Designing simple algorithms for localization and discovery
of nodes, time synchronization.
Media Access Control (MAC) layer issues:
  Collision avoidance
  Topology control for higher energy efficiency
  Trade-off between energy efficiency and latency, errors
  Bandwidth utilization
  Scalability in node density
  Reduce idle listening, collisions, control overheads, overhearing
  Improve physical/ radio layer performance
Key technical challenges faced

## Slide 23
Fast information retrieval:
Topology adaptation and control:
  Topology adaptation for higher node density, Environmental
  changes, Redundant deployments
  Topology control schemes such as sharing workload within
  cluster, removal of redundant links, data driven schemes
Key technical challenges faced

## Slide 24
For further queries,
Kindly contact:
Prof. Ravindra Joshi
Associate Professor, Dept. of Engg. Sciences
International Institute of Information Technology (I2IT)
Email: ravindraj@isquareit.edu.in
Cell: 9822021594