## Slide 1
Pulse Modulation
Smita R Kadam
Department of Electronics and Telecommunication
International Institute of Information Technology, I²IT
www.isquareit.edu.in

## Slide 2: Modulation Techniques
In continuous wave modulation technique amplitude, frequency or phase of a sinusoidal carrier can be modulated with a information signal
Since sine wave is used as the carrier signal it is termed as continuous wave modulation
In pulse modulation, pulse train is used as a carrier signal
Amplitude, frequency or phase (position) of pulses in a pulse train can be modulated with an information signal is Pulse modulation
Pulse analog modulation techniques are of three types PAM,PWM and PPM
Coded pulse modulation is pulse amplitude modulation in which pulse amplitudes are transmitted in a binary code
Fundamental and most important pulse digital modulation technique is the Pulse code Modulation (PCM)

## Slide 3
Types of Modulation
Pulse Code Modulation
Frequency Modulation
Analog Modulation
Digital Modulation
Angle modulation
Amplitude Modulation
Pulse Modulation
Continuous wave Modulation
Delta Modulation
PWM
PPM
PAM
Phase Modulation
PWM
PAM
CLASSIFICATION

## Slide 4: Pulse Amplitude Modulation
Process of varying the amplitude of the pulse in proportion to the instantaneous variations of message signal
C(t) is a periodic pulse train with a period of Ts
Pulse amplitude modulated wave in time domain is obtained by multiplying the message signal with the pulse train
The amplitude of the PAM signal follows the message signal contour
The message signal is a low frequency signal
PAM signal results in convolution of their spectra in the frequency domain
Spectrum of PAM signal is in low frequency range
PAM is found to be useful in sampling process

## Slide 5: Pulse Amplitude Modulation (PAM)
Message signal, m(t)
Periodic Pulse train, c(t)
Naturally sampled signal ,s(t)
-5Ts -4Ts -2T -Ts 0 Ts 2Ts 4Ts
τ
t
t
t

## Slide 6: Pulse width Modulation PWM
In pulse modulation techniques if the frequency and amplitude of a pulse train are kept constant and the width of the pulse is varied with a modulating signal then the result is PWM
Width of the pulse train in PWM is proportional to instantaneous amplitude of message signal
for positive values of message pulse width proportionally increases and for negative values decreases proportionally
PWM is more robust to noise than PAM
Width modulation of pulse is done using leading edges or using trailing edge or using both(centre)
PWM signal also contain message information but seldom used in sampling as randomness is involved in message information
Limited use in signal processing and in communication filed

## Slide 7
Pulse Width Modulated signal
Modulating Signal
PWM with lead edge fixed
PWM with trailing edge fixed
PWM with centre fixed
Periodic pulse train
t
t
t
t
t
Leading Edge
Trailing Edge
Notes: ht7i

## Slide 8: PWM generation by Comparator
Inverter
Differentiator
Edge triggered pulse generator
PPM
output
PWM
input
PWM
output
Input message
Saw tooth
-
+
b. PPM generation from PWM
a. PWM generation by a Comparator

## Slide 9: PWM generator
A comparator is given two inputs, message signal and carrier signal
Maximum of the input signal, should be less than carrier then PWM is generated at the output of comparator
Minimum of carrier should be less than minimum of message signal
When positive of comparator is at higher potential output is positive and
When negative of comparator is at higher potential output is negative
Duration for which comparator stays high is dependent on input signal magnitude and this decides width of pulse generated
Thus width of the pulse generated at its output is proportional to the amplitude of message signal at that instant

## Slide 10: PPM Generation
PWM generated signal is sent to an inverter to reverses polarity of the pulses
Differentiator will generate positive spikes where original PWM signal was going from HIGH to LOW and
Negative spikes where LOW to HIGH transition
Positive edge triggered pulse generator ,generates pulses of fixed width when a positive spike appears , coinciding with falling edge of original PWM
PPM outputs where positions of pulses carry input message information
Randomness of the width in PWM and randomness in position of pulse in PPM do not make them suitable for time division multiplexing scheme

## Slide 11: PWM application
Speed control of DC motor using PWM:
Speed of DC motor depends on the average DC voltage applied across its terminals
Case
‘V ‘ volts is the voltage for running the DC motor
‘0’ volts rest condition for DC motor
Now speed of DC motor can be varied from rest to full speed value by varying the DC voltage controlled by PWM
PWM provides a convenient and efficient approach for the speed control of DC motor
refer the link https://youtu.be/3To3Zgr1Jao to learn execution of this project

## Slide 12: Pulse Position Modulation (PPM)
Process of varying the position of the pulse with respect to the instantaneous variations of the message signal
If ‘tp‘ indicates the timing instant of the leading or trailing edge of the pulse in each period of the pulse train, In PPM tp α vm
Mathematically position of the leading or trailing edge of the pulse in PPM signal is given by
tp = f(vm ) position of pulse is function of message signal instantaneous amplitude
When there is no message, position of leading/trailing edge of the pulse is equal to the original position tp = 0
For positive values of message , the position will be proportionately shifted right
For negative values of message, the position will be proportionately shifted left

## Slide 13
PWM signal
Modulating Signal
PWM with leading edge fixed
PAM signal
Pulse locations are
same but their
widths change
Pulse widths are
same but their
locations change
PPM Signal
t
t
t
t
Pulse Modulation Techniques
Notes: ht7i

## Slide 14: Demodulation of Pulse amplitude Modulated Signals
PPM can be generated by processing PWM
Edge of the PWM waveform is detected to get position of the pulse in each period
PWM can be generated by processing PPM
PAM,PWM and PPM stores the message in the baseband itself
The message information here is represented at discrete instants of time
Demodulator can reconstruct the approximate version of the continuous time signal
When PAM input is passed through Low Pass Filter , it retains low frequency information and smoothes out the pulse train information
PWM and PPM signals are first converted into PAM and then perform low pass filtering

## Slide 15: Demodulation of Pulse Analog Modulated Signals
PWM / PPM
to PAM converter
Low Pass Filter
PWM
Message
signal
PPM
Low Pass Filter
Message
signal
PAM

## Slide 16: Pulse Code Modulation (PCM)
The fundamental and most important pulse digital modulation technique is the Pulse Code Modulation
In PAM amplitude can take on any value over a continuous range
Digital signal amplitude can take on only a finite number of values
PCM represents each discrete amplitude level by a binary code
PCM is a tool for converting Analog signal into Digital signal (ADC)
Low Pass Filter also acts as a anti aliasing filter
Sampler block essentially performs PAM process
Input of the sampler block is a signal which is continuous in time and amplitude
While output of sampler has a signal which is discrete in time and continuous in amplitude (value)

## Slide 17: PCM system Diagram
Low Pass Filter
Sampler
Quantizer
Bit
Encoder
Message
signal
input
1 1 0 1
PCM wave

## Slide 18: Quantization -PCM
Round a group of nearby amplitude values and represent them by a single discrete amplitude value is Quantization
The signal with discretized amplitude values is termed as Quantized signal
Assigned single discrete amplitude value is called quantized Level (here L1 to L8)
Amplitudes of analog signal m(t) is divided into uniform or non uniform intervals as Uniform or Non-uniform Quantization
Here total number of amplitude levels from mp to -mp into 8 levels
Thus each analog value is sampled by PAM process, quantized and
represented by a binary word of 3 bits (so total levels that can be represented would be 23= 8 levels)

## Slide 19
L4 - 011
L3 - 010
L2 - 001
L1 - 000
L8 -111
L7 - 110
L6 - 101
L5 - 100
QUANTIZATION of sampled analog signal
mp
mp

## Slide 20
Output of the quantizer will have a signal which is discrete both in time and amplitude
The output of the encoder will have a unique binary code for each discrete amplitude value
The whole process of sampling , quantizing and encoding is also termed as Analog to Digital Conversion (ADC) operation
For any analog signal output of ADC is PCM signal
Quantization Noise : Error between original analog signal and its allocated quantized version

## Slide 21: Case study- Telephone signal
Audio signal bandwidth is about 15KHz
For speech signal all signals above 3400Hz(fm) are eliminated by Low Pass Filter
Resulting signal is then sampled at a rate of 8000 (fs) samples per second (8KHz) ( fs >= 2fm) sampling theorem
Rate is kept higher than Nyquist sampling rate of 6.8KHz so that realizable filters can be applied for signal reconstruction
Quantization levels are 256 (L-256)
256 levels means each level requires a group of 8 binary pulses to encode each sample (28=256)
Each sample in this example is encoded by 8 binary bits
Thus, a telephone signal requires 8 x 8000 = 64,000 binary pulses per second

## Slide 22: Case study - Compact Disc (CD)
This is a case where high-fidelity is desired
Required audio signal bandwidth 20KHz
Actual sampling rate 44.1 KHz (rather than 40KHz as per Nyquist rate)
The signal is quantized into L= 65,536 quantization levels
To reduce quantization error each of the level is represented with 16 bits
The binary coded samples are then recorded on the Compact Disc with 1.4 million bits/sec (2 channel)

## Slide 23: References
R Taub, D Schilling and G Saha, Principles of Communication Systems, 3rd edition, Mc Graw Hill, 2012
D Roddy, J Coolen, Electronic Communication, 4th edition, Pearson, 2011
G Kennedy, B Davis, S R M Prasanna, Electronic Communication Syatems,5 th edition, Mc Graw Hill, 2011
B P Lathi, Zhi Ding, Modern Digital and Analog Communication systems, 4th edition

## Slide 24
Thank You!!
For any queries
Contact: smitak@isquareit.edu.in